Spaghetti Bridge Assignment Sheet

Each group is to build a bridge made from spaghetti and plain Elmer’s glue. The object is to construct a bridge that will carry the heaviest load while still meeting all of the requirements.  We will add weight to the bridges until they fail.

RULES:

1. The bridge is to be built only from spaghetti and glue.

2. The bridge is to be free-standing and must span two level surfaces which are 10 inches apart.

3. The bridge must be at least 5cm wide across the full span of the bridge. The surface of the bridge that a car would drive on must be covered so that a matchbox car could drive across it without falling through. (Except for the hole that must be left on the deck of the bridge for testing.)

4. The bridge will be graded on its efficiency.

(THIS MEANS THAT FOR A HEAVY BRIDGE TO WIN, IT WILL HAVE TO HOLD MUCH MORE THAN A LIGHT BRIDGE)